## Slide 1: Beyond Vision
Beniamin
  Tech enthusiast &
  Hardware researcher
  3nd year Computer engineering student
Advisor:
Alin Grama

## Slide 2: Steganography
Steganography is the art and science of sending covert message and the existence of these messages are only known by the sender and the receiver.
This technique has been practiced for thousands of years.

## Slide 3: Benefits of steganography
Highly securely
Could be very useful in copyright

## Slide 4: Benefits of steganography
Could not be traced
Allows encrypted communicates without being detected

## Slide 5: Is steganography really useful?
British Prime Minister Margaret Thatcher used this to identify the internal informer
US and USSR were transmitting information about nuclear facilities on public channels without revealing the receiver location
You may not be the only one reading your private messages on social media, steganography can stop it

## Slide 6: My solution
A highly secure server which is hardware accelerated to embed and extract hidden data inside images, sound and encrypt data faster

## Slide 7
So how does it work?

## Slide 8: Performance > 300% faster
Chart: 
| Encryption[mS] | Decrypt[mS] | Filter for Encryption | Filter for Decryption | Overall
Software implementation | 34.4 | 36.9 | 39.37 | 39.37 | 42.81
Hardware implementation | 17.2 | 21.8 | 0.8775 | 0.8775 | 4.5975
Chart: Image processing time
| 640x480 | 1280x720 | 1920x1080 | 3840x2160
Software | 157.98 | 373.4 | 787.4 | 1919.5
Hardware | 2.68 | 7.86 | 17.55 | 69.67

## Slide 9: Comparison
 | Medium computer CPU + Memory + Motherboard + Power supply + Storage + Case | ARM/FPGA
Price | > 2000 lei | 1600 lei
Power on load | >300W | 4.1W
Monthly cost | > 200 lei | 10 lei

## Slide 10
Main features?
Hardware accelerated:
  Cryptography algorithms (RSA)
  Image Steganography
  Sound Steganography
True random number generator for generating certificates
External HDMI video processor
Easily integrated with exposed API
Chat App integrated
Real time operating system
Drivers for Linux Kernel developed

## Slide 11
Development Stages
Exploring possibilities
and research
Develop HDMI processing unit
Build hardware for Linux Kernel
Modifying and compiling Linux
Develop Linux module to work with HDMI
Create hardware modules for encryption and decryption
Create hardware modules for random generator
Web service
Presentation
Refactoring

## Slide 12: Further development
Parallelization more the encryption and decryption to get better performances
Optimize architecture
Accelerate multiple video algorithms

## Slide 13
What we used in order to create the platform:
Notes: In order to develop this we have used: POZE CU LOGOURI SI ZENZORI <- DE ADAUGAT